## Slide 1: SIGNALS, SYSTEMS, AND SIGNAL PROCESSING
Signal
Convey information from one point to another (They may be generated by electronic means, or by some natural means such as talking, walking, your heart beating, an earthquake, the sun heating the sidewalk)
described by a function of one or more independent variables. The value of the function (i.e., the dependent variable) can be real-valued scalar quantity a complex-valued quantity or perhaps a vector.
Examples: , ,

## Slide 2: SIGNALS, SYSTEMS, AND SIGNAL PROCESSING
System
process signals to produce a modified or transformed version of the original signal
defined as a physical device that performs an operation on a signal.
Example. A filter used to reduce the noise and interference corrupting a desired information-bearing signal is called a system.
Signal Processing –the operation on or analysis of signals, or measurements of time-varying or spatially varying physical quantities.

## Slide 3: Basic Elements of a Digital Signal Processing System

## Slide 5: Multichannel and Multidimensional Signals

## Slide 8: Continuous-Time versus Discrete Time Signals
Discrete- time signals are defined only at certain specific values of time. To emphasize the discrete- time nature of a signal, we shall denote such a signal as or x[n] instead of If the time instants are equally spaced (i.e., ), the notation is also used.
Graphical representation of the discrete time signal for and for

## Slide 9: Continuous-Time versus Discrete Time Signals
Continuous- time signals or analog signals are defined for every value of time and they take on values in the continuous interval (a, b), where a can be and b can be .
Example. Speech waveform, signals ,
Example of a speech signal

## Slide 10: Continuous-Valued versus Discrete-Valued Signals
Continuous- Valued Signals- if a signal takes on all possible values on a finite or an infinite range.
Discrete –Valued Signal – if the signal takes on values from a finite set of possible values.

## Slide 11: Deterministic vs Random Signals
Deterministic - Any signal that can be uniquely described by an explicit mathematical expression, a table of data, or a well-defined rule.
Random - are signals that either cannot be described to any reasonable degree of accuracy by explicit mathematical formulas, or such a description is too com plicated to be of any practical use

## Slide 12: Discrete-Time Signal or Sequence
Graphically, it can be represented as

## Slide 13: Discrete Time Signals or Sequence
Besides the graphical, there are some alternative representation:
Functional representation
Tabular representation
n | … | -2 | -1 | 0 | 1 | 2 | 3 | 4 | …
x[n] | … | 0 | 0 | 0 | 1 | 4 | 1 | 0 | …

## Slide 14: Discrete Time Signals or Sequence
Besides the graphical, there are some alternative representation:
Sequence Representation
  An infinite-duration signal or sequence with the time origin ) indicated by the symbol ↑ is represented as
  A sequence x[n], which is zero for , can be represented as
  A finite –duration sequence can be represented as
  whereas a finite-duration sequence that satisfies the condition x[n] = 0 for n < 0 can be represented as
  x[n] = { 0, 1, 4, 1}

## Slide 15: SEATWORK
A discrete time signal is defined as
A. Give the graphical, tabular and sequential representation of the given functional representation.

## Slide 16: Some Elementary Discrete Time Signal
Unit Sample Sequence
  a signal that is zero everywhere except at where its value is unity. Denoted by
  It is sometimes referred to as a unit impulse.
  Functional representation
  Graphical representation

## Slide 17: Some Elementary Discrete Time Signal
Unit Step Signal
  Denoted by u[n]
  Functional representation
  Graphical representation
u

## Slide 18: Some Elementary Discrete Time Signal
Unit Ramp Signal
  denoted by

## Slide 19: Some Elementary Discrete Time Signal
Exponential signal
  A sequence of the form
  Graphical representation (Parameter a is real)

## Slide 20: Some Elementary Discrete Time Signal
Exponential signal (cont…)
  Graphical representation (Parameter a is complex-valued)
  where r and θ are now parameters.
  ∴

## Slide 21: Some Elementary Discrete Time Signal
Graph of amplitude and phase function of a complex-valued exponential signal

## Slide 22: Classification of Discrete-Time Signals
Energy signals and Power Signals
Energy signals
  The energy E of a signal x[n] is defined as
  It can be finite or infinite.
    If E is finite (i.e , , then x[n] is called an energy signal.
Notes: We have used the magnitude squared values of x[n], so that our definition applies to complex-valued signal as well as real-valued signals.
Sometimes we add a subscript x to E to emphasize that 𝐸_𝑥 is the energy of the signal x[n].

## Slide 23: Classification of Discrete-Time Signals
Power Signal
  Many signals that possess infinite energy, have a finite average power.
  It is defined as .
    If we define the signal energy of x[n] over the finite interval as
    =
    Signal energy can be expressed as
    The average power of the signal x[n] as
  If E is finite, . On the other hand, if E is infinite, the average power may be either finite or infinite.
  If P is finite(and nonzero), the signal is called a power signal.

## Slide 24: Sample Problems:
Determine the power and energy of the unit step sequence.
Find the power and signal energy of
Find the power and signal energy of .
Find the power and signal energy of.
Find the signal energy of .
Find the power and signal energy of

## Slide 25: Classification of Discrete-Time Signals
Symmetric(Even) and Antisymmetric (Odd)
  A real-valued signal x[n] is called symmetric(even) if
  A real-valued signal x[n] is called antisymmetric(odd) if
  Examples of signals with even and odd symmetry.

## Slide 26: Classification of Discrete-Time Signals
Symmetric(Even) and Antisymmetric (Odd)
  Even Signal Component
  Odd Signal Component
  Any arbitrary signal can be expressed as

## Slide 27: Sample Problem:
Find the even and odd part of the function
What are the even and odd parts of the function
What are the even and odd parts of the function

## Slide 28: Classification of Discrete-Time Signals
Periodic and Aperiodic Signals
  A signal x[n] is periodic with period if and only if
  for all n.
  If there is no value of N that satisfies the equation above, the signal is called non periodic or aperiodic.
  Periodic signals are power signal.
  N = fundamental period in discrete time. N must be a positive integer.
  fundamental angle of frequency or discrete angle of frequency. It is denoted as
  Frequency is denoted as

## Slide 29: Simple Manipulation of Discrete-Time Signals
In this section we consider some simple modifications or manipulations involving the independent variable and the signal amplitude (dependent variable).
Transformation of the independent variable(time)
A signal x[n] may be shifted in time by replacing the independent variable n by n , where k is an integer.
  If k is a positive integer, the time shift results in a delay of the signal by k units.
  If k is a negative integer, advance the signal by k.

## Slide 30: Simple Manipulation of Discrete-Time Signals
Transformation of the independent variable(time) (cont…)
Example:
The signal is graphically illustrated below:
Show the graphical representation of (a) and (b)

## Slide 31: Simple Manipulation of Discrete-Time Signals
Transformation of the independent variable(time) (cont…)
Folding or reflection
  Replace the independent variable n by –n.
  The result of this operation is a folding or a reflection of the signal about the time origin .
Example.
Show the graphical representation of the signal and , where x[n] is the signal illustrated in the previous slide.
Notes: It is important to note that the operations of folding and time delaying (or advancing) a signal are not commutative. If we note the time-delay operation by TD and the folding operation by FD, we can write
〖𝑇𝐷〗_𝑘 {𝑥[𝑛]}=𝑥[𝑛−𝑘] 𝑘>0
𝐹𝐷 {𝑥[𝑛]}=𝑥[−𝑛]
Now
〖𝑇𝐷〗_𝑘 {𝐹𝐷(𝑥[𝑛])}=〖𝑇𝐷〗_𝑘 {𝑥[−𝑛]}=𝑥[−𝑛+𝑘]
Wheras
𝐹𝐷{〖𝑇𝐷〗_𝑘 (𝑥[𝑛])}=𝐹𝐷{𝑥[𝑛−𝑘]}=𝑥[−𝑛−𝑘]

## Slide 32: Simple Manipulation of Discrete-Time Signals
Transformation of the independent variable(time) (cont…)
Time Scaling or Down Sampling
  A third modification of the independent variable which involves by replacing by by 𝛍n, where 𝛍 is an integer.
Example. Show the graphical representation of the signal
, where x[n] is the signal illustrated below.

## Slide 33: Simple Manipulation of Discrete-Time Signals
Addition, multiplication, and scaling of sequences
  Amplitude scaling of a signal by a constant A is accomplished by multiplying the value of every signal sample by A.
  Addition of sequences or signal
    The sum of two signals and is a signal , whose value at any instant is equal to the sum of the values of these two signals at the instant
  Product of sequences or signal
    The product of two signals is similarly defined on a sample-to-sample basis as
Notes: Example:

## Slide 34: DISCRETE TIME SYSTEMS
It is a device or algorithm that operates on a discrete-time signal (input or excitation) to produce another discrete-time signal (output or response).
            Block diagram representation
We say that the input signal x[n] is transformed by the system into a signal y[n] and express the general relationship between x[n] and y[n] as
Notes: In general, we may view a system as an operations performed on the input x[n] to produce the output signal y[n].
𝓣 denotes transformation (also called an operator), or processing performed by the system on x[n] to produce y[n]. The mathematical relationship in equation above is depicted graphically in figure above.

## Slide 35: Input-Output Description of the System
It consists of a mathematical expressions or rule, which explicitly defines the relation between the input and output signals (input-output relationship).
Aside from the previous figure and equation, alternatively, we use the notation
Notes: The exact internal structure of the system is either unknown or ignored. Thus the only way to interact with the system is by using its input and output terminals(i.e., the system is assumed to be a” black box” to he user.
Graphically same as figure in the previous slide as well as the equation.
It simply means that y[n] is the response of the system 𝒯 to the excitation x[n].

## Slide 36: Input-Output Description of the System
Example:
Determine the response of the following the systems to the input signal

## Slide 37: Block Diagram Representation of Discrete-Time Systems
Adder

## Slide 38: Block Diagram Representation of Discrete-Time Systems
Constant Multiplier

## Slide 39: Block Diagram Representation of Discrete-Time Systems
Signal Multiplier

## Slide 40: Block Diagram Representation of Discrete-Time Systems
Unit delay element
Notes: The unit delay is a special system that simply delays the signal passing through it by one sample. The given figure illustrates such a system. If the input signal is x[n], the output is x[n-1]. In fact, the sample x[n-1] is stored in memory at time n-1 and it is recalled from the memory at time n to form 𝑦[𝑛]=𝑥[𝑛−1].

## Slide 41: Block Diagram Representation of Discrete-Time Systems
A unit advance element

## Slide 42: EXAMPLE NO. 1
x[n]
+
+
5/6
1
-1/6
y[n]
Give the input-output relation of the given system above

## Slide 43: EXAMPLE NO. 2
Using basic building blocks introduced, sketch the block diagram representation of the discrete time system described by the input-output relation
where x[n] is the input and y[n] is the output of the system.

## Slide 44: EXAMPLE NO. 3
Using basic building blocks introduced, sketch the block diagram representation of the discrete time system described by the input-output relation
where x[n] is the input and y[n] is the output of the system.