## Slide 1: Basic Measurement Theory
Measurement
The art or process of determining the amount, quantity, degree, or capacity by comparison with accepted standards of the system of units employed.
is defined as the process of comparison of an unknown quantity with a known or standard quantity.

## Slide 2
NEED OF MEASUREMENT
Establish standard
Interchangeability
Customer Satisfaction
Validate the design
Physical parameter into meaningful number
True dimension
Evaluate the Performance

## Slide 3
METHODS OF MEASUREMENT
Direct method
Indirect method
Comparative method
Coincidence method
Contact method
Deflection method
Complementary method

## Slide 4
DIRECT METHOD
Measurements are directly obtained
Ex: Vernier Caliper, Scales
INDIRECT METHOD
Obtained by measuring other quantities
Ex: Weight = Length x Breadth x Height x Density

## Slide 5
Analog and Digital
Vernier Caliper
Analog and Digital Micrometer

## Slide 6
COMPARATIVE METHOD
It’s compared with other known value
Ex: Comparators
COINCIDENCE METHOD
Measurements coincide with certain lines and signals

## Slide 7
FUNDAMENTAL METHOD
Measuring a quantity directly in related with the definition of that quantity
CONTACT METHOD
Measuring tip touch the surface area
Ex: Sensors

## Slide 8
COMPLEMENTARY METHOD
The value of quantity to be measured is combined with known value of the same quantity
Ex: Volume determination by liquid displacement

## Slide 9
DEFLECTION METHOD
The value to be measured is directly indicated by a deflection of pointer
Ex: Pressure Measurement
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 10: Units and Standards (SI: Fundamental Units)
Physical Quantity | Unit Name | Symbol
Length | meter | m
Mass | kilogram | kg
Time | seconds | s
Electric Current | ampere | A
Temperature | Kelvin | K
Luminous Intensity | candela | Cd

## Slide 11: Units and Standards (SI: Derived Units)
Physical Quantity | Unit Name | Symbol
Area | square meter | m²
Volume | cubic meter | m³
Speed | meter per second | m/s
Acceleration | meter per second squared | m/s²
Force | Newton | N
Pressure | Pascal | P

## Slide 12: Units and Standards (SI: Derived Units)
Physical Quantity | Unit Name | Symbol
Energy, Work | Joule | J
Electromotive Force | Volt | V
Quantity of charge | Coulomb | C
Electrical Resistance | Ohm | Ω
Capacitance | Farad | F
Inductance | Henry | H

## Slide 13
MEASUREMENT STANDARDS
International standards
Defined by international measurement,
Paris International Bureau of Weight and
Measurement.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 14
MEASUREMENT STANDARDS
Primary standards
Principal functions is the calibration and
verification of Secondary standards,
National Standards Laboratory
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 15
MEASUREMENT STANDARDS
Secondary standards
Basic reference standards,
Industrial Laboratory
Working standards
Principal tools of a measurement laboratory
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 16
Characteristics of Measuring Instrument
Readability
Is defined as the closeness with which the scale of the analog instrument can be read.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 17
Characteristics of Measuring Instrument
Range of accuracy
Accuracy of a measuring system is defined as the closeness of the instrument output to the true value of the measured quantity.
Accuracy is the quality of conformity.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 18
Characteristics of Measuring Instrument
Precision
Is defined as the ability of the instrument to reproduce a certain set of readings within a given accuracy
The precision of a measurement depends on the instrument used to measure it.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 19
Error
Is the deviation of the true value from the desired value.
Measurement error can be random or systematic and it affects the quality of measurements and the reliability of statistical analyses.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 20
Types of Errors
Error of Measurement
Instrumental Error
Error of Observation
Based on Nature of Errors
Based on Control
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 21
3 Types of Measurement Errors
1. Gross error
are generally caused by the instrument users.
Ex: incorrect reading of instrument
incorrect recording of data
incorrect use of instruments
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 22
3 Types of Measurement Errors
2. Systematic error
Are due to problems of instruments, environmental errors and observational errors.
3. Random error
Neither Gross or Systematic error
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 23
Systematic Errors
a. Instrument errors – due to friction with the bearing of the meter movement, incorrect spring tension, improper calibration or faulty instruments. It can be reduced by proper maintenance, proper use and handling of instruments.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 24
Systematic Errors
b. Environment errors – instruments are subjected to harsh environments such as high temperature, pressure, or humidity or strong electrostatic or electromagnetic fields. May have detrimental effects causing errors.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 25
Systematic Errors
c. Observational errors – errors introduced by the observer. Two most common are parallax error – introduced by reading a meter scale and the error of estimation – when obtaining a reading from a meter scale.
Units and standards
SI: fundamental Units
Physical Quantity Unit Name Symbol
Length meter mMass kilogram kgtime second selectric current ampere Atemperature Kelvin Kamount of substance mole molluminous intensity candela cd

## Slide 26: ERROR IN MEASUREMENT
Absolute Error
e = Yn – Xn
where e = absolute error
Yn = expected value
Xn = measured value
Expected value – quantitative measurement of the so called true value / most probable value.

## Slide 27: ERROR IN MEASUREMENT
Percentage Error
% error = x 100
By substitution:
% error = || x 100

## Slide 28: ERROR IN MEASUREMENT
Relative Accuracy
A = 1 - ||
where A = relative accuracy
Percent Accuracy
a = 100% - % error
a = A x 100

## Slide 29
Example: the expected value of the voltage across a resistor is 50 V. Measurement yields a value of 49 V. Calculate the (a) absolute error (b) % error (c ) relative accuracy and
(d) percentage accuracy.

## Slide 30
Solution:
a) e = Yn – Xn
= 50 V – 49 V
e = 1 V
b) % error =||x 100
= || x 100
% error = 2 %

## Slide 31
Solution:
c) A = 1 - ||= 1 - ||
A = 1 - ||
A= 0.98
d) a = 100% - % error
a = 100% - 2%
a = 98%

## Slide 32
Precision – a measure of the consistency or repeatability of measurements.
Precision = 1 - ||
where Xn = the value of the nth measurement
xn = the average of the set of n measurement

## Slide 33
Basic Instrument System
Most modern analog equipment works on the following standard signal ranges:
Electric – 4 mA to 20 mA
Pneumatic – 0.2 bar to 1.0 bar
Older electrical equipment uses 0 to 10 V.

## Slide 34
Basic Instrument System
As of now, the instruments are digital with a binary digital encoder built in to give a binary digital output.
Pneumatic signals are commonly used in process industries for safety especially when there is a risk of fire or explosion.

## Slide 35
Things that are commonly measured:
Temperature Pressure
Speed Flow rate
Force Movement, Velocity and Acceleration
Stress and Strain Level or Depth
Mass or Weight Density
Size or Volume Acidity/Alkalinity

## Slide 36
Sensors may operate simple on/off switches to detect the following:
Objects (Proximity switch)
Empty or full (level switch)
Hot or cold (thermostat)
Pressure high or low (pressure switch)